## Slide 1: netflow

## Slide 2: What is Netflow
Feature/network protocol that was introduced on Cisco routers
Netflow records the communication between systems. Traffic that enters or exits an interface
Routers/switches that support NetFlow collects IP traffic statistics and export those statistics to a NetFlow collector
By analyzing flow data a picture of network traffic flow, volumne and peak time can be built
Can be used to spot anomalies
Simple IDS capabilities

## Slide 3: What is Netflow
Very fast – only takes up about 0,01% of traffic capture
Cons
Does not provide content of the traffic
Only an indication of what has happend

## Slide 4: Netflow typical record
Source and destination IP address
Source and destination ports
Transport protocol: TCP, UDP, ICMP, etc.
Type of service (ToS)
Packet and byte counts
Start and end timestamps
Input and output interface numbers
TCP flags
Routing information (next-hop address, source autonomous system (AS) number, destination AS number, source prefix mask, destination prefix mask)

## Slide 5: Create netflow data

## Slide 6: 1 tcp connection => 2 flows
Computer a web browse computer b => 2 flows
Request flow: A: (TCP) 1.2.3.4:3365 -> 4.3.2.1: 80
Reply flow: B: (TCP) 4.3.2.1:80 -> 1.2.3.4:3365

## Slide 7: One tcp connection => 2 flows

## Slide 8: Netflow limitation of cache
Difficult to read
Only shows recent activity
No automation on devices for analysis
No accounting of flows (besides overall totals)

## Slide 9: NetFlow Export of Data
Greatly enhances NetFlow and turns the technology into a analysis tool!
Data sent to external collector(s)
Analyzed by one or more systems
Archived for other concerns
Efficient: Uses multiple records per UDP packet

## Slide 10: Typical netflow collector setup

## Slide 11: Full capture vs netflow
A combination of Netflow and FPC will often be considered the best solution.
Netflow sensors on all routers but only FPC on critical segments.
Rotate FPC after 1 week and netflow after 365 days.

## Slide 12: Netflow components
fprobe - This is the exporter that export flows in the form of flow records.
nfcapd - This is the collector. Recieves flow records from 1 or more exporters, parsing and storing the information.
nfdump This is the analysis tool, that enables us to query the netflow data

## Slide 13: Setting up netflow
Install fprobe and nfdump
apt-get update
apt-get install fprobe
apt-get install nfdump
Let fprobe export all traffic on eth0 as netflow to collector (running on port 555)
fprobe -i eth0 localhost:555
Collect the netflow data on port 555 and write it to the disk
Mkdir netflow
nfcapd -D -p 555 -S 1 -z -I Linux-Host-1-eth0 -l /root/netflow/
Extract netflow traffic from FPC
nfcapd -r dmp.pcap -S 1 -z -l /root/netflow/

## Slide 14: Looking into netflow
root@allan-VirtualBox:/root# mkdir netflow
root@allan-VirtualBox:/root# nfcapd -D -p 555 -S 1 -z -I Linux-Host-1-eth0 -l /root/netflow/
root@allan-VirtualBox:/root/netflow# nfcapd -r dmp.pcap -S 1 -z -l /root/netflow/
root@allan-VirtualBox:/root/netflow# ls
2017 nfcapd.current
root@allan-VirtualBox:/root/netflow/2017/12/11# nfdump -r nfcapd.201712112200 (PING REQUEST)
Date flow start Duration Proto Src IP Addr:Port Dst IP Addr:Port Packets Bytes Flows
2017-12-11 21:59:20.962 0.000 UDP 10.0.2.13:5353 -> 224.0.0.251:5353 1 131 1
2017-12-11 21:59:22.120 0.000 UDP 212.242.40.3:53 -> 10.0.2.18:42430 1 126 1
2017-12-11 21:59:22.119 0.000 UDP 212.242.40.51:53 -> 10.0.2.18:42430 1 126 1
2017-12-11 21:59:22.022 0.000 UDP 10.0.2.18:42430 -> 212.242.40.3:53 1 51 1